DECREE OF THE DIRECTOR GENERAL OF POST AND TELECOMMUNICATION

NUMBER: 268/DIRJEN/2005

ON

TECHNICAL REQUIREMENTS OF TOOLS AND EQUIPMENT OF DIGITAL SATELLITE SET TOP BOX

BY THE GRACE OF GOD THE ALMIGHTY

DIRECTOR GENERAL OF POST AND TELECOMMUNICATION

Considering:          a.  that   the   Decision   of   the   Minister of   Communication

Number:   KM 3  Year 2001 on Technical Requirements of

Telecommunication  Tools  and   Equipment stipulates that

every telecommunication tool and equipment shall fulfil the

technical requirements;

- that in order to implement the provision of Article 3 of the  Decree of the Minister of Communication Number: KM.10 Year 2005 on Certification of Telecommunication Tools and Equipment, any testing of telecommunication tools and equipment must be based on technical requirements as determined by the Director General;

- that in view of what is stated in points a and b above, it is considered necessary to ratify a Decree of the Director General of Post and Telecommunication on Technical Requirements   of   Tools and Equipment of Digital Satellite Set Top Box.

Bearing in mind: 1.  Law of the Republic of Indonesia Number 36 Year 1999 on

Telecommunication   (State Gazette  of   the   Republic   of

Indonesia   Number   154   Year  1999,   Additional    State

Gazette of the Republic of Indonesia Number 3881);

- Government Regulation of the Republic of Indonesia Number 52 Year 2000 on Provision of Telecommunication (State Gazette of the Republic of Indonesia Number 107 Year 2000, Additional State Gazette of the Republic of Indonesia Number 3980);

- Government Regulation of the Republic of Indonesia Number 53 Year 2000 on Use of Radio Frequency Spectrum and Satellite Orbit (State Gazette of the Republic of Indonesia Number 108 Year 2000, Additional State Gazette of the Republic of Indonesia Number 3981);

- Decree of the President of the Republic of Indonesia Number 9 Year 2005 on Positions, Tasks, Functions, Organizational Structure and Working of State Ministries  of the Republic of Indonesia;

- Decree of the President of the Republic of Indonesia Number 10 Year 2005 on Organizational Units and Functions of Echelon I of State Ministries of the Republic of Indonesia as amended by the Decree of the President of the Republic of Indonesia Number 15 Year 2005;

- Decision of the Minister of Communication Number KM.3 Year 2001 on Technical Requirements of Telecommunication Tools and Equipment;

- Decree of the Minister of Communication Number KM.10 Year 2005 on Certification of Telecommunication Tools and Equipment;

- Decree of the Minister of Communication and Information Technology Number 01/P/M.Kominfo/1/2005 on Organizational Structure and Working of the Department of Communication and Information Technology.

DECIDES

To ratify            :	DECREE OF THE   DIRECTOR   GENERAL  OF  POST AND

TELECOMMUNICATION ON TECHNICAL  REQUIREMENTS                      OF TOOLS AND EQUIPMENT OF DIGITAL SATELLITE SET TOP BOX

Article 1

The Tools and Equipment of Digital Satellite Set Top Box shall fulfil the technical requirements as indicated in the Attachment of this Decree.

Article 2

The implementation of certification of tools and equipment of Digital Satellite Set Top Box shall be guided by the technical requirements as stipulated in Article 1

Article 3

This Decree shall come into force as from the date of its ratification.

Done at:             JAKARTA

On       :  October 12, 2005

_____________________

DIRECTOR GENERAL OF POST AND TELECOMMUNICATION

Signed

BASUKI YUSUF ISKANDAR

Copies of this Decree are sent to:

- Minister of Communication and Information Technology;

- Secretary of the Directorate General of Post and Telecommunication;

- Directors within the Directorate General of Post and Telecommunication;

- Head of the House of Telecommunication Equipment Testing.

ATTACHMENT :  DECREE OF THE DIRECTOR GENERAL

OF POST AND TELECOMMUNICATION

NUMBER          :  268/DIRJEN/2005

DATE                :  October 12, 2005

________________________________________________

TECHNICAL REQUIREMENTS OF TOOLS AND EQUIPMENT OF DIGITAL SATELLITE SET TOP BOX

CHAPTER I

GENERAL PROVISIONS

- Scope

These technical requirements are the ones for the equipment of digital receiver of set top box. These requirements cover scope, definitions, abbreviations, configuration, technical requirements, special function requirements for subscriber TV and testing requirements.

- Definition

What is meant by Equipment of Digital Satellite Set Top Box is receiver of television broadcast through Satellite media.

- Abbreviations

AM	:  	Amplitude Modulation

DVB	:	Digital Video Broadcasting

IEC	:	International Electrotechnical Commission

LNB	:	Low Noise Block

MPEG	:	Moving Picture Experts Group

PAL	:	Phase Alternation Line

RF	:	Radio Frequency

STB	:	Set Top Box

QPSK	:	Quadrature Phase Shift Keying

- Configuration

CHAPTER II

TECHNICAL REQUIREMENTS

- General

  - Voltage Input                                             : 90 -240 Volt AC

  - Electrical voltage of electrical frequency   : 50 Hz ± 5%

  - Temperature range                                   : 0oC – 50o C

  - Humidity range                                          : 5% - 95%

- System

System of capability fully DVB – S Compliant

- Tuner

  - IF Frequency Input                                   : 950 – 2150 MHz

  - IF Connector Input                                    : F Type / IEC 169-24

  - Impedance Input                                       : 75 Ώ

  - Level signal input                                      : -25 ~ -65 dBm

  - LNB Control                                              : Diseq 1.0 / 22 KHz

  - LNB voltage and polarization                    : 13 V / 18 V

- Canal Decoder

  - Demodulation                                           : QPSK ( SCPC, MCPC )

  - Rack Symbol Input                                   : 2 – 45 Msps

  - Forward Error correction                          : ½, 2/3, ¾ , 5/6, 7/8

- Video

  - Level Profile                                             : MPEG II  MP@ML

  - System Output                                         : PAL B/G (minimum requirement)

  - Terminal Output                                       : 1 x RCA and/or 1 x BNC

  - Level Output                                             :

  - Impedance                                                : 75 Ώ

- Audio

  - Audio Decoder                                          : MPEG I & MPEG II Layer I & II

  - Sample Level                                            : 32/44, 1/48 KHz

  - Frequency Response                                : 20 Hz – 20 KHz

  - Impedance                                                : 600 Ώ

  - Terminal Output                                        : 2 x RCA

- Radio Frequency (RF)

  - Frequency Output                                     : 470 – 862 MHz (Selectable)

  - RF Level Output                                        : 60 dBµV – 80 dBµV

  - Impedance                                                : 75 Ώ

  - Modulation                                                : AM

  - RF Terminal                                              : F Type / IEC Connector

- IF Loop Through

    - Loop Terminal                                           : F Type / IEC169-24

    - Impedance                                                : 75 Ώ

CHAPTER III

SPECIAL FUNCTION REQUIREMENTS FOR SUBSCRIBER TV

Support Conditional Access System for receiving subscriber TV broadcast.

CHAPTER IV

TESTING REQUIREMENTS

- Method of Selecting Testing Sample

Selection of testing materials is carried out by random sampling by the testing authority with the minimum number of 2 sample materials.

- Testing Method

The testing method is defined by the testing institution which must be capable of showing in a qualitative and quantitative manner that the testing materials are measured according to the testing procedure and requirements in this standard.

- Conditions for Passing the Test

The testing result is declared PASS THE TEST, if all the testing materials comply with the provisions contained in the technical requirements.

- Conditions of Labelling

Every Set Top Box equipment shall be labelled, containing the name of the manufacturer and manufacturing country, brand/type and serial number and must fulfil the conditions of certification.

Done at:              JAKARTA

On        :  October 12, 2005

______________________

DIRECTOR GENERAL OF POST AND TELECOMMUNICATION,

Signed

BASUKI YUSUF ISKANDAR